## Slide 1: The Noise Measured by Back-illuminated Silicon Sensors
Roy T. Smart1, Charles C. Kankelborg1, and Jacob D. Parker2
1Montana State University
2NASA/GSFC
246th Meeting of the American Astronomical Society
June 9th, 2025
Notes: Hi everyone, thanks for joining me today, my name is Roy Smart and I am a PhD student at Montana State University.
Today I’d like to talk about some work that we did on modeling the noise measured by back-illuminated silicon imaging sensors that are often used in astrononmy.

## Slide 2: IRIS Noise Mystery
IRIS measures less noise than predicted (Wulser et al. 2018).
  Photon transfer curve is too shallow
    Expected slope ratio > 2
    Measured slope ratio = 1.5
  SNR is ~25% better than expected
Notes: An I’d like to begin with a minor mystery: on the left are two photon-transfer curves for the Interface Region Imaging Spectrograph, or IRIS from Wulser et al 2018.
A photon transfer curve plots the observed variance of a flat field as a function of the mean value.
The top plot is a photon-transfer curve in blue light and the bottom is the same but for ultraviolet light at 1350 angstroms.
From theoretical considerations, the IRIS team expected that the slope ratio between these two curves to be greater than 2 but they measured only 1.5
This is good news, as IRIS has about 25% better signal-to-noise ratio than expected, but why?

## Slide 3: HST/WFC3 Noise
Wide Field Camera 3 (WFC3) on Hubble also has this issue (Marinelli & Green 2024)
  “Quantum yield” is lower
    Expected ~1.7 @ 200 nm
    Measured 1.09 @ 200 nm
  SNR is ~25% better than expected

## Slide 4: Outline
Signal
  Quantum yield
  Charge-collection efficiency
  Absorption
Noise
  Simple noise model
  Shot noise
  Fano noise
  Partial-charge collection noise
Results

## Slide 5: Signal

## Slide 6: Quantum Yield
Quantum yield (QY) is the number of electron-hole pairs generated per photon
QY increases as photon energy increases
  QY = E / (3.65 eV) where E is the energy of the photon
Ramanathan & Kurinsky (2020) QY model

## Slide 7: Back-illuminated Sensor Model
Thin layer of silicon dioxide (~1 nm)
Light-sensitive silicon (16 μm)
  Partial-charge collection (PCC) region (~100 nm)
  Field-free region
  Depletion region (8 μm)

## Slide 8: Partial-Charge Collection
Photons are absorbed according to the Beer-Lambert law (red)
Photons absorbed in PCC region lose some electrons
Charge-collection efficiency (CCE) is the fraction of charge measured.
Piecewise-linear differential CCE introduced by Stern et al. (1994)
  Denoted

## Slide 9: Penetration depth
Some ultraviolet wavelengths have a penetration depth smaller than the PCC region
  ~40 – 100 A
  ~500 – 4500 A
Sensor is much less efficient in these regions
Notes: This is a plot of pen depth vs wavelength. PCC happens near the surface, so only wavelengths that dip below this line are significantly affected by PCC.
Twin axes for CCE

## Slide 10: Average Charge-Collection Efficiency
Integrate Beer-Lambert law against differential CCE
Average CCE is needed for correct photometry
Notes: This is a plot of pen depth vs wavelength. PCC happens near the surface, so only wavelengths that dip below this line are significantly affected by PCC.
Twin axes for CCE

## Slide 11: Absorbance
Energy absorbed by light-sensitive layer
  Reflections from each interface
  Oxide absorption
  Transmittance through entire sensor
Computed using standard optical constants (Henke 1993, Palik 1997)
Notes: This is a plot of pen depth vs wavelength. PCC happens near the surface, so only wavelengths that dip below this line are significantly affected by PCC.
Twin axes for CCE

## Slide 12: Quantum Efficiency
Quantum Efficiency (QE) is the factor used to convert from incident photons to measured electrons
Allowed to be larger than one!

## Slide 13: Effective Quantum Efficiency (EQE)
Measured quantity
  Compare sensor to NIST photodiode
Between 0 and 1
Often used to compute QE

## Slide 14: Noise

## Slide 15: Variance-to-mean ratio
Convenient measure of noise
  If is Poisson-distributed,
Constant vs. signal, unlike SNR
Equal to the slope of the photon-transfer curve
Same units as

## Slide 16: Simple Noise Model
Shot noise only
All-or-nothing charge collection
Used by IRIS and WFC3

## Slide 17: A Slightly More Complicated Noise Model
Shot noise
Fano noise
  Inherent randomness in the charge-generation process
PCC noise
  Uncertain CCE due to random absorption depth

## Slide 18: Shot Noise
Absorbed photons are Poisson-distributed

## Slide 19: Fano Noise
Quantum yield uncertainty
Described by Fano factor
Ramanathan & Kurinksy (2020) QY model
Small compared to other noise sources

## Slide 20: PCC Noise
Since each photon is absorbed at a different depth, each experiences a different CCE.

## Slide 21: Total Noise
Sum of shot, Fano, and PCC noise
VMR is smaller than the simple model in the UV
The partial events improve the noise performance

## Slide 22: SNR improvement
SNR improves by up to compared to the simple model

## Slide 23: Charge spreading?
Charge spreading is when electrons diffuse into adjacent pixels.
Proportional to size of field-free region
Could explain the discrepancy since this increases the correlations between pixels
Stern et al. (2003)

## Slide 24: Mean Charge Capture (MCC)
Average fraction of charge captured by central pixel
Janesick (2001) charge spreading model
Stern et al. (2004) measurements
Fit size of field-free region
Predicts a similar amount of charge spreading for both UV and visible light

## Slide 25: Compare to Measurements

## Slide 26: Affected Instruments
AIA
  94 Å
  1600 Å
  1700 Å
IRIS
  1330 Å
  1400 Å
MUSE
  108 Å

## Slide 27: Conclusions
Partial-charge collection is mostly responsible for IRIS noise mystery
Charge spreading is less important
Need to use a more complicated expression to compute noise
The model predicts better SNR in some wavelengths than designers expected
Results affect AIA, IRIS, WFC3, ESIS, FURST, and MUSE.
Code provided in the optika.sensors Python module.
  Published on PyPI